## Slide 1: Introduction to the Thumb Instruction Set
CDAC Mumbai

## Slide 2: Agenda
Thumb Register Usage
ARM-Thumb Interworking
Other Branch Instructions
Data Processing Instructions
Single Register Load Store Instructions
Multiple Register Load Store Instructions
Stack Instructions
Software Interrupt Instruction
Summary

## Slide 3: Thumb Instruction Set
Thumb encodes a subset of the 32 bit ARM instructions into a 16 bit instruction set space
Thumb has higher performance than ARM on a processor with a 16 bit data bus
Use thumb for memory constrained systems
Thumb has higher code density
30% less memory than the equivalent ARM implementation

## Slide 4: Code Density
ARM Code
ARMDivide
;IN : ro(value),r1(divisor)
;OUT : r2(MODulus),r3(DIVide)
MOV r3,#0
loop
SUBS r0,r0,r1
ADDGE r3,r3,#1
BGE loop
ADD r2,r0,r1
5 x 4 = 20 bytes
Thumb Code
ThumbDivide
;IN : ro(value) ,r1(divisor)
;OUT : r2(MODulus) ,r3(DIVide)
MOV r3,#0
loop
ADD r3,#1
SUB r0,r1
BGE loop
SUB r3,#1
ADD r2,r0,r1
6 x 2 = 12 bytes

## Slide 5: Thumb Instruction Decoding
D
E
C
O
D
E
R
ADD r0,#3
ADDS r0,r0,#3
Thumb 16 bit instruction
ARM 32 bit instruction
cpsr=nzcvqifT_SVC

## Slide 6: Thumb Instruction Set
Mnemonics | THUMB ISA | Description
ADC | v1 | add two 32 bit values & carry
ADD | v1 | add two 32 bit values
AND | v1 | logical bitwise AND of two 32 bit values
B | v1 | branch relative
BIC | v1 | logical bit clear of two 32 bit values
BKPT | v2 | breakpoint instructions
BL | v1 | relative branch with link
BLX | v2 | branch with link and exchange
BX | v1 | branch with exchange
CMN | v1 | compare negative two 32-bit values
CMP | v1 | compare two 32 bit values
EOR | v1 | logical EOR of two 32 bit values

## Slide 7: Thumb Instruction Set
Mnemonics | THUMB ISA | Description
LDM | v1 | load multiple 32 – bit words from memory to ARM registers
LDR | v1 | load a single value from a virtual address in memory
LSL | v1 | logical shift left
LSR | v1 | logical shift right
MOV | v1 | move a 32 bit value into a register
MVN | v1 | move the logical NOT of 32 bit value into a register
MUL | v1 | multiply two 32 bit values
NEG | v1 | negate a 32 bit value
ORR | v1 | logical bitwise OR of two 32 bit values
POP | v1 | pops multiple registers from the stack
PUSH | v1 | pushes multiple registers to the stack
ROR | v1 | rotate right a 32 bit value

## Slide 8: Thumb Instruction Set
Mnemonics | THUMB ISA | Description
SBC | v1 | subtract with carry a 32 bit value
STM | v1 | store multiple 32 bit registers to memory
STR | v1 | store register to a virtual address in memory
SUB | v1 | subtract two 32 bit values
SWI | v1 | software interrupt
TST | v1 | test bit of a 32 bit value

## Slide 9: Thumb Register Usage
Registers | Access
r0 - r7 | fully accessible
r8 – r12 | only accessible by MOV, ADD & CMP
r13sp | limited accessibility
r14lr | limited accessibility
r15pc | limited accessibility
cpsr | only indirect accessible
spsr | no access

## Slide 10: ARM – Thumb Interworking
Method of linking ARM and Thumb code together
T bit of the cpsr
BX & BLX cause a switch between ARM & Thumb state while branching to a routine
BX lr instruction returns from a routine
BX instruction enters thumb state only if bit 0 of the address in Rn is set to binary 1

## Slide 11: ARM – Thumb Interworking
BX Rm
BLX Rm | label
BX | Thumb version branch exchange | pc = Rn & 0xfffffffe T = Rn[0]
BLX | Thumb version branch exchange with link | lr = (instruction address after BLX)+1 pc = label, T = 0 pc = Rm & 0xfffffffe T = Rm[0]

## Slide 12: Other Branch Instructions
B <cond> label
B label
BL label
B | branch | pc = label
BL | branch with link | pc = label lr = (instruction address after the BL)+1
Notes: MOV pc,lr
BX lr
POP {pc}

## Slide 13: Data Processing Instructions
<ADC|ADD|AND|BIC|EOR|MOV|MUL|NEG|ORR|SBC|SUB> Rd, Rm
<ADD|ASR|LSL|LSR|ROR|SUB> Rd, Rn #immediate
<ADD|MOV|SUB> Rd, #immediate
ADD Rd, pc, #immediate
ADD Rd, sp, #immediate
<ADD|SUB> sp, #immediate
<ASR|LSL|LSR|ROR> Rd, Rs
<CMN|CMP|TST> Rn, Rm
CMP Rn, #immediate
MOV Rd, Rn

## Slide 14: Data Processing Instructions
ADC | add two 32 bit values & carry | Rd=Rd+Rm+C flag
ADD | add two 32 bit values | Rd=Rn+immediate Rd=Rd+immediate Rd=Rd+Rm Rd=(pc&0xfffffffc)+(immediate <<2) Rd=sp+(immediate <<2) sp=sp+(immediate <<2)
AND | logical bitwise AND of two 32 bit values | Rd=Rd&Rn
ASR | arithmetic shift right | Rd=Rm>>immediate C flag = Rm[immediate-1] Rd=Rd>>Rs,C flag=Rd[Rs-1]

## Slide 15: Data Processing Instructions
BIC | logical bit clear (AND NOT) of two 32 bit values | Rd=Rd AND NOT (Rm)
CMN | compare negative two 32 bit values | Rn + Rm set flags
CMP | compare two 32 bit values | Rn-immediate set flags Rn-Rm set flags
EOR | logical exclusive OR of two 32 bit values | Rd = Rd EOR Rm
LSL | logical shift left | Rd=Rm<<immediate C flag = Rd[32-immediate] Rd=Rd<<Rs, C flag=Rd[32-Rs]

## Slide 16: Data Processing Instructions
LSR | logical shift right | Rd=Rm>>immediate C flag = Rd[immediate-1] Rd=Rd>>Rs,C flag=Rd[Rs-1]
MOV | move a 32 bit value into a register | Rd = immediate Rd = Rn Rd = Rm
MUL | multiply two 32 bit values | Rd=(Rm*Rd)[31:0]
MVN | move the logical NOT of a 32 bit value into a register | Rd=NOT (Rm)
NEG | negate a 32 bit value | Rd=0-Rm

## Slide 17: Data Processing Instructions
ORR | logical bitwise OR of two 32 bit values | Rd=Rd OR Rm
ROR | rotate right a 32 bit value | Rd=Rd RIGHT_ROTATE Rs, C flag = Rd[Rs-1]
SBC | subtract with carry a 32 bit value | Rd=Rd-Rm-NOT(C flag)
SUB | subtract two 32 bit values | Rd=Rn-immediate Rd=Rd-immediate Rd=Rn-Rm sp=sp-(immediate<<2)
TST | test bits of a 32 bit value | Rn AND Rn set flags

## Slide 18: Single Register Load Store Instructions
<LDR|STR>{<B|H>} Rd, [Rn, #immediate]
LDR{<H|SB|SH>} Rd, [Rn, Rm]
STR{<B|H>} Rd, [Rn, Rm]
LDR Rd, [pc, #immediate]
<LDR|STR> Rd, [sp, #immediate]
Type | Syntax
Load/Store Register | [Rn, Rm]
Base Register+offset | [Rn, #immediate]
Relative | [pc¦sp, immediate]
Addressing Modes

## Slide 19: Single Register Load Store Instructions
LDR | load word into a register | Rd<-mem32[address]
STR | save word from a register | Rd ->mem32[address]
LDRB | load byte into a register | Rd<-mem8[address]
STRB | save byte from a register | Rd ->mem8[address]
LDRH | load halfword into a register | Rd<-mem16[address]
STRH | save halfword from a register | Rd ->mem16[address]
LDRSB | load signed byte into a register | Rd <–SignExtend (mem8[address])
LDRSH | load signed halfword into a register | Rd <–SignExtend (mem16[address])

## Slide 20: Multiple Register Load Store Instructions
<LDM|STM>IA Rn!, {low register list}
N is the number of registers in the list of registers.
These instructions always update the base register Rn after execution
The base register and list of registers are limited to the low registers r0 to r7
LDMIA | load multiple registers | {Rd}*N <- mem32 [Rn + 4 * N], Rn = Rn + 4 * N
STMIA | save multiple registers | {Rd}*N -> mem32 [Rn + 4 * N], Rn = Rn + 4 * N

## Slide 21: Stack Instructions
POP {low_register_list{,pc}}
PUSH {low_register_list{,lr}}
There is no stack pointer in the instruction. The stack pointer is fixed as register r13 in thumb operations and sp is automatically updated
POP | pop registers from the stacks | {Rd}*N <- mem32 [sp + 4 * N], sp = sp + 4 * N
PUSH | push registers on to the stacks | {Rd}*N -> mem32 [sp + 4 * N], sp = sp + 4 * N

## Slide 22: Software Interrupt Instructions
SWI immediate
If any interrupt or exception flag is raised in Thumb state, the processor automatically reverts back to ARM state to handle the exception
SWI | software interrupt | lr_svc =address of instruction following the SWI spsr_svc = cpsr pc = vectors + 0x8 cpsr mode = SVC cpsr I = 1 (mask IRQ interrupts) cpsr T = 0 (ARM state)

## Slide 23: Summary
All Thumb instructions are 16 bit in length
Thumb provides approx. 30% better code density over ARM code
ARM Thumb interworking – BX, BLX
Only branch instructions are conditionally executed
Multiple register load store instructions only support the increment after (IA) addressing mode
There is no Thumb instructions to access the coprocessor, cpsr, spsr