## Slide 1: Embedded Systems
CDAC Mumbai

## Slide 2: Embedded Systems
Definition:-
“ An embedded system is a microcontroller based software driven, real time control system, which may be autonomous or human or network interactive, operating on diverse physical variables and in diverse environments”

## Slide 3: Where do we find Embedded Systems
Home appliances
  Microwave ovens, washing machines,
Entertainment devices
  TV, DVD players, MP3 players
Telecommunication
  Mobile phones, Telephones
Computers
  Keyboards, Disk drives
Automobiles
  Dashboard, Fuel Injection, suspension, GPS

## Slide 4: Characteristics
Principal function is control and not computation
Usually designed to perform selected functions at a low cost
Microcontroller or Microprocessor is embedded
Firmware is embedded in hardware devices
Programs need to run with real-time constraints with limited hardware resources
  These systems meet their real-time constraints with a combination of special purpose hardware and software tailored to the system requirements.
Embedded systems reside in machines that are expected to run continuously for years without errors.
  the software and Firmware is usually developed and tested more carefully than Software for Personal computers
Some embedded system may be outside the reach of humans

## Slide 5: Subsystems
Three main subsystems
  Microcontroller
  Memory
    To store program
    To store data
  Input Output
  Interconnecting elements

## Slide 6: Microcontroller Characteristics
Input/Output intensive
‘on-chip’ peripherals
Physically small
Simple program and data storage requirement
Instruction set optimised for embedded environment
  Yields compact code
  Limited arithmetic capability
  Limited addressing capability
  Strong in bit manipulation
Low cost
Extended temperature range/low power

## Slide 7: Processor Architecture (Memory)
Single Main Memory holding both program and data
Simple memory structure
Data memory is idle when program is fetched
Storing or modifying programs is easy
Bottleneck on buses
Pin count is reduced
  Ex. 8085, x86
Contains two separate memory spaces- code & data
Complex memory Structure
Instructions can be fetched simultaneously with instruction execution
Princeton or Von-neuman
Harvard

## Slide 8: Processor Architecture (Memory)
Princeton or Von-neuman
Harvard
CPU
PROGRAM MEMORY
DATA MEMORY, PERIPHERALS
DATA BUS
ADDRESS BUS
CPU
PROGRAM MEMORY
DATA MEMORY, PERIPHERALS
DATA BUS
ADDRESS BUS
DATA BUS
ADDRESS BUS

## Slide 9: Processor Design
Microprocessors are Instruction Set Processors(ISP)
  Executes instructions from a predefined instruction set
  Functionality is characterized by the instruction set it is capable of executing
  All programs that run on it are encoded in that instruction set
  This predefined instruction set is also called as Instruction Set Architecture (ISA)
ISA serves as an interface between
  Hardware and software
  Programs and processor
Performance Equation
time program
time cycle
cycles instruction
instructions program
X
X
=

## Slide 10: Instruction Set Architectures (ISA)
Reduced Instruction Set Computer
RISC approach attempts to reduces the cycles per instruction at the cost of the number of instructions per program.
Emphasis on software
Fixed length instructions
Large Register bank
Load & Store Architecture
Complex Instruction Set Computer
CISC approach attempts to minimize the number of instructions per program, sacrificing the number of cycles per instruction.
Emphasis on hardware
Variable length instruction
Small Register Bank
Memory Operands
RISC
CISC

## Slide 11: Instruction Set Architectures (ISA)
Nearly all instructions executes in fixed time.
Few addressing Modes
Efficient instruction pipeline
Less silicon area required, so more peripherals added
Variable execution time for Instructions.
Many Addressing Modes
Mostly not implement any pipelining
More silicon area required, very few peripherals may added
RISC
CISC

## Slide 12: Life Cycle of an Instruction
As the instruction moves through the processor it goes through the following stages.
  Fetch : Instruction fetched from the address stored in the program counter.
  Decode : Instruction decoded and registers read
  Execute : in the ALU
  Write back : Results written back to registers or memory.
• Note : each stage takes one clock cycle
• The Instruction execution requires 4 clock cycles

## Slide 13: Non Pipelined Example
2 instructions take 4ns each
A stage is used once every 4ns
The resultant throughput is 4 cycles per instruction (CPI)

## Slide 14: Pipelined Example
Each stage is utilized at every clock cycle.
5 Instructions are executed in 8ns
Resultant throughput is 1 instruction per cycle

## Slide 15: Memory
Characteristics of ideal memory
  Read and writes cycles should be fast
  Large amount of information should be held in small space, dense
  Data should be held indefinitely, even when power is removed, non-volatile
  Low power consumption, with convenient supply voltage requirement
  High reliability and durability

## Slide 16
IO devices are treated as like memory
Memory related instructions should be used to access IO
IO devices are separately interfaced
Separate instruction set available
Memory Mapped IO
IO Mapped IO

## Slide 17: Memory Classification
Semiconductor Memory
Volatile
Non- Volatile
Static
Mask Programmable ROM
Fuseable ROM
‘Field Alterable’ ROM
EPROM
EEPROM
Flash
Dynamic

## Slide 18: The Memory Array
Solid state memory is made of large number of memory cells each of which hold one bit of information
A number of fundamentally different methods are used to achieve storage in memory cell
  A bistable element as in CMOS static RAM
  Electrical charge stored in a capacitor as in DRAM
  Electrical charge trapped on a conductor as in EPROM, EEPROM and Flash
  Presence or absence of electrical connection between two conductors as in PROM

## Slide 19: DRAM
Uses ‘memory’ capability of capacitor
Ideal capacitor when charged will hold its charge indefinitely and voltage can be read
Memory cell is made up of single storage capacitor and switching transistor
Charged capacitor represents logic 1
When cell transistor is switched on by word line, capacitor voltage is connected to bit line
High density memory can be made at comparatively low cost
Capacitor charge leaks and the cell has to be refreshed every 100 ms
This is cumbersome and discourages its use in smaller embedded system

## Slide 20: SRAM
CMOS SRAM cells are bistable (flip-flop) cells
They are usually made of either four transistors and two resistors(4T-2R pattern) or of six transistors(6T)
Due to low density, size of RAM is small. Usually a few Kilobytes

## Slide 21: EPROM
Charge can be transferred to floating gate, if drain and gate terminals are raised to high potential
Some electrons gain enough energy to gather on floating gate. This is called hot electron injection
This charge is trapped once the programming voltage is removed.
This charge alters the threshold voltage as seen by the control gate, the transistor can no longer be turned on.
Drain Gate Source
Control Gate
Floating Gate
Substrate
Si02 insulator

## Slide 22: EPROM
Can be programmed in parts
Erasure of selected parts is not possible
Erasure is slow
In-circuit erasure and programming not possible
EPROMs have achieved wide usage in microcontroller world and many microcontrollers are available with integral EPROMs
Ceramic packaging and quartz window increases the price

## Slide 23: EEPROM
Memory cell uses FNT (Fowler-Nordheim Tunneling) mechanism for transferring electron through SiO2
Insulating layer thickness is of the order of 10nm
FNT takes much less current than hot electron injection
On chip voltage converters develop the supply voltages required
Structures are so designed that FNT effect can be reversed, so cells can be both programmed and erased electrically
Needs two transistor per cell, one with floating gate, another for bit-select

## Slide 24: EEPROM Contd..
Programming and Erasure cycles tend to take different time durations
Time can vary from cell to cell and depends on cell age, as charge can become trapped in insulating oxide layers
Electrical erasure is susceptible to risk of accidental programming due to power change.
Endurance figure is specified by manufacturer, the max. number of permissible erase/write cycles
This figure applies to every memory location
EEPROM is very popular in microcontroller world
  Embedded into the microcontroller
  Physically outside as small serial device

## Slide 25: Flash Memory
Most recent and is developing fastest
It is not byte erasable, whole block need to be erased
High density, low cost, non-volatile, fast (to read, but not to write), and electrically reprogrammable.
These advantages are overwhelming and, as a direct result, the use of flash memory has increased dramatically in embedded systems.
Most common Flash cell is ETOX (EPROM Tunnel Oxide) developed by Intel
On chip EPROM program memories of Microcontroller are getting replaced by Flash
  Simpler packing is cheaper
  In system programmable
Flash will also replace EEPROM, except where byte programmability of EEPROM is indispensable.

## Slide 26: Input Output
On-Chip
  Common peripherals are found on most uCs
    UART, Digital IO, ADC , TIMER
  Application Specific peripherals on custom uCs
    LCD, IrDA, USB, CAN
Off-Chip
  Flexibility to choose controller
  Port pins have to used
  Needs extra Space

## Slide 27: IO Communication
A Microcontroller system must manage its communication with the device it is controlling
  Programmed IO
    CPU takes or delivers data under control of program
  Interrupt Driven
    Peripheral grabs attention of CPU when it is ready
  DMA
    Used for transferring large chunks of data
    Not very popular with small systems

## Slide 28: Managing I/O
Two common ways of managing communication
  Polling
  Interrupt

## Slide 29: Polling
Purpose: Allows the CPU to determine the status of an I/O device..
Mechanism:
  The CPU regularly polls the I/O device to determine the device’s status.
  Polling requires that the CPU actively ask devices what is happening.
Polling Examples:
  Has a switch been thrown?
  Has an error condition occurred?
  Is the data from the device ready yet?
  Is the device ready to receive the data yet?

## Slide 30: Polling Flowchart
Reset
Initialise
Check Device 1 status
Check Device N status
Service Device 1
Service Device N
Device needs Service
Device needs Service

## Slide 31: Polling
Polling advantages:
  The software to implement polling is straight forward.
Polling disadvantages:
  The CPU must interact with the device even when no service is needed.
  Polling response time can be long.
    This is the delay between the time a device needs service and the time the CPU provides service.
    The more devices that must be polled, the longer the polling response time.

## Slide 32: Interrupts
Purpose:
  Allows a device to get the attention of the CPU
Mechanism:
  Special interrupt signals are hooked to the CPU.
When one or more of these signals are asserted, the CPU is interrupted.
When interrupted, the CPU stops doing what it was doing and jumps to an interrupt service routine (ISR).
The ISR executes code to communicate with the I/O device.
When the ISR is done, the CPU resumes the task it was doing before it was interrupted.

## Slide 33: Interrupt Flowchart
Reset
Initialise
Save State & Disable Interrupts
Clear Interrupt Request
Main Loop
ISR
Service Device
Restore State & Enable Interrupts

## Slide 34: Interrupt
Advantages:
  The CPU must interact with devices only when they need service.
  The interrupt response time is usually lower than the polling response time.
Disadvantages:
  The software to implement interrupt support is more complex than it is for polling.