## Slide 1
Data
Communication
&
Networking

## Slide 2
➲
➲
➲
➲
➲
Networks,connectivity......
Topologies....
Multiplexing
Protocols
Reference Layer Models....
Overview
Overview

## Slide 3
Information, Computers, Networks
• Information: anything that is represented in
bits
– Form (can be represented as bits) vs
– Substance (cannot be represented as bits)
• Properties:
– Infinitely replicable
– Computers can “manipulate” information
– Networks create “access” to information

## Slide 4
Networks
• Potential of networking:
– move bits everywhere, cheaply, and with
desired performance characteristics
– Break the space barrier for information
• Network provides “connectivity”

## Slide 5
What is “Connectivity” ?
• Direct or indirect access to every other
node in the network
• Connectivity is the magic needed to
communicate if you do not have a direct
pt-pt physical link.
– Tradeoff: Performance characteristics worse than
true physical link!

## Slide 6
Connectivity.
• Building Blocks
– links: coax cable, optical fiber..
– nodes: general-purpose workstations...
• Direct connectivity:
– point-to-point
– multiple access

## Slide 7
Connectivity..
• Indirect Connectivity
– switched networks
=> switches
– inter-networks
=> routers

## Slide 8
Connectivity …
• Internet:
– Best-effort
(no performance
guarantees)
– Packet-by-packet
• A pt-pt physical link:
– Always-connected
– Fixed bandwidth
– Fixed delay
– Zero-jitter

## Slide 9
Point-to-Point Connectivity
• Physical layer: coding, modulation etc
• Link layer needed if the:
– link is shared between apps (framing, medium
access control, multiplexing)
– link is unreliable (reliability)
– link is used sporadically and traffic can flood
receivers (flow control)
• No need for protocol concepts like addressing,
names, routers, hubs, forwarding, filtering …
A
B

## Slide 10
Connecting N users: Directly ...
• Bus: broadcast, collisions, media access
control
• Full mesh: Cost vs simplicity
...
Full mesh
Bus
receiver alone to consume the packet!

## Slide 11
List of Problems (so far)
•
•
•
•
•
Topologies
Framing
Error control
Flow control
Multiple access
– How to share a wire

## Slide 12
How to build Scalable Networks?
• Scaling: system allows the increase of a
key parameter. Eg: let N increase…
– Inefficiency limits scaling …
• Direct connectivity is inefficient & hence
does not scale
– Mesh: inefficient in terms of # of links
– Bus architecture: 1 expensive link, N cheap
links. Inefficient in bandwidth use

## Slide 13
Filtering, forwarding …
• Filtering: choose a subset of elements
from a set
– Filtering is the key to efficiency & scaling
• Forwarding: actually sending packets to a
filtered subset of link/node(s)
– Packet sent to one link/node => efficient
• Solution: Build nodes which filter/forward
and connect indirectly => “switches” &
“routers”

## Slide 14
S
Connecting N users: Indirectly
• Star: One-hop path to any node, reliability,
forwarding function
• “Switch” S can filter and forward!
– Switch may forward multiple pkts in parallel for
additional efficiency!
Star

## Slide 15
Connecting N users: Indirectly …
• Ring: Reliability to link failure, near-minimal
links
• All nodes do “forwarding” and “filtering”
Ring

## Slide 16
S
Ring
Star
Tree
Topologies: Indirect Connectivity

## Slide 17
Inter-Networks: Networks of
Networks
=
Internet
…
…
…
…
Our goal is to design this black box on the right

## Slide 18
Inter-Networks: Networks of
Networks
• Internetworking involves two fundamental
problems: heterogeneity and scale
• Concepts:
– Translation, overlays, address & name resolution,
fragmentation: to handle heterogeneity
– Hierarchical addressing, routing, naming, address
allocation, congestion control: to handle scaling

## Slide 19
Additions to Problem List
• Fragmentation
• Switching, bridging,
routing
• Naming, addressing
• Congestion control,
traffic management
• Reliability

## Slide 20
How to do system design ?
• Eg goal: Design an Inter-network…
• Resources:
–
–
–
–
–
Space
Time
Computation
Money
Labor
• Design: trade-off cheaper resources
against expensive ones to meet goals.

## Slide 21
Building blocks: Multiplexing
• Multiplexing = sharing
– Trades time and space for money
– Cost: waiting time, buffer space & packet loss
– Gain: Money => Overall system costs less

## Slide 22
Statistical Multiplexing
• Reduce resource requirements by exploiting
statistical knowledge of the system.
– Eg: average rate <= service rate <= peak rate
– If service rate < average rate, then system
becomes unstable!!
• First design to ensure system stability!!
– Then, for a stable multiplexed system:
• Gain = peak rate/service rate.
• Cost: buffering, queuing delays, losses.

## Slide 23
Stability of a Multiplexed System
Average Input Rate > Average Output Rate
=> system is unstable!
How to ensure stability ?
• Reserve enough capacity so that
demand is less than reserved capacity
• Dynamically detect overload and adapt
either the demand or capacity to resolve
overload

## Slide 24
What’s a performance tradeoff ?
• R=link bandwidth
(bps)
• L=packet length
(bits)
• a=average packet
arrival rate
Traffic intensity = La/R
• A situation where you cannot get something
for nothing!
• Also known as a zero-sum game.

## Slide 25
What’s a performance tradeoff ?
• La/R ~ 0: average
queuing delay small
• La/R -> 1: delays
become large
• La/R > 1: average delay
infinite (service degrades
unboundedly =>
instability)!

## Slide 26
Example Design: Circuit-Switching
– Divide link bandwidth
into “pieces”
– Reserve pieces on
successive links and tie
them together to form a
“circuit”
– Map traffic into the
reserved circuits
– Resources wasted if
unused: expensive.
– Mapping can be done without “headers”.
– Everything inferred from timing.
Circuit-switching: A form of multiplexing

## Slide 27
– Chop up data (not links!)
into “packets”
• Packets: data + meta-data
(header)
– “Switch” packets at
intermediate nodes
• Store-and-forward if
bandwidth is not immediately
available.
Bandwidth division into
“pieces”
Dedicated allocation
Resource reservation
Example Design: Packet-Switching
Packet-switching: Another form of multiplexing:

## Slide 28
Packet Switching
A
B
C
10 Mbs
Ethernet
45 Mbs
statistical multiplexing
1.5 Mbs
queue of packets
waiting for output
link

D E
Cost: self-descriptive header per-packet,
buffering and delays for applications.

dynamically detect/adapt to overload for stability

## Slide 29
Summary of System Design Ideas
• Multiplexing
• Statistical Multiplexing
• Stability and
performance tradeoffs
• Circuit switching
• Packet switching

## Slide 30
What are protocols ?
• Networking software is organized as protocols
• Eg: Human protocol vs network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://www.rpi.edu/index.htm
<file>
time

## Slide 31
Analogy: Organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
• Protocols: a series of functions
performed at different locations

## Slide 32
Organization of air travel: a different
view
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Layers: each layer implements a service
– via its own internal-layer actions
– relying on services provided by layer below
interface

## Slide 33
Layered air travel: services
Counter-to-counter delivery of person+bags
baggage-claim-to-baggage-claim delivery
people transfer: loading gate to arrival gate
runway-to-runway delivery of plane
airplane routing from source to
destination
Similarly, we organize network protocols
into a bunch of layers!

## Slide 34
Departing
airport
arriving
airport
Distributed implementation of layers
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
intermediate air traffic sites
airplane routing
airplane routing

## Slide 35
Protocol Implementations
• Are building blocks of a network architecture
• Each protocol object has two different interfaces
– service interface: defines operations on this
protocol
– peer-to-peer interface: defines messages
exchanged with peer
service interface
peer interface
Li+1
Li
Li+1
Li

## Slide 36
Reference Models for Layering
Session
Transport
Network
Datalink
Physical
Transport
Internetwork
Host to
Network
TCP
UDP
IP
EtherPacket Point-to-
net Radio Point
TCP/IP Model
Application
OSI Ref Model
Application
Presentation
TCP/IP Protocols
FTP Telnet HTTP
“Top-down” approach means we will first learn the
application layer and then learn about lower layers

## Slide 37
Internet protocol stack
• application: supporting network
applications
– ftp, smtp, http
• transport: host-host data transfer
– tcp, udp
• network: routing of datagrams
from source to destination
– ip, routing protocols
• link: data transfer between
neighboring network elements
– ppp, ethernet
• physical: bits “on the wire”
application
transport
network
link
physical

## Slide 38
Layering: logical communication
data
application
E.g.: transport
• take data from
app
• add addressing,
reliability check
info to form
“datagram”
• send datagram
to peer
• wait for peer to
ack receipt
• analogy: post
office
transport
network
link
physical
application
transport
network
link
physical
ack network
link
data physical
data
application application
transport transport
network network
link link
physical physical

## Slide 39
application |  | 
physical |  | 
application | 
transport | 
 | link
physical | 
link | 
physical | 
Layering: physical communication
application
transport
network
link
physical
network
link
physical
data
data

## Slide 40
Protocol layering and data
Each layer takes data from above
• adds header information to create new
data unit (“encapsulation”)
• passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
Ht M
HnHt M
Hl HnHt M
M
M
M
M
Ht
HnHt
Hl HnHt
message
segment
datagram
frame

## Slide 41
Summary
•
Networks, connectivity, topologies …
• Idea about networking layers ...
•

## Slide 42
Thank U